## Slide 1: VHDL_02: More RTL Block Design
Topics
  Using default statements for combinational processes
  Three types of RTL blocks:
    counters
    shift-registers
    finite state machines
  UART- Receiver : requirements for design (Lab-2)
  Design Partitioning (divide and conquer :o)

## Slide 2: VHDL_02: More RTL Block Design
Examples
  COUNT_DOWN.VHD
  ALARM_LEVEL_DISPLAY_WO_DEFAULT.VHD
  ALARM_LEVEL_DISPLAY.VHD
  SHIFTREG_P2S.VHD
  SYNC_N_EDGEDETECTOR.VHD
  FSM_EXAMPLE.VHD
  FSM_EXERCISE.VHD

## Slide 3: VHDL_02: More RTL Block Design
Laboratory
  Design of a UART receiver (UART-RX) with:
  Baud rate: 31250 bits per second
  Serial input via GPIO pin in extension header of the board
  Display each received byte into two seven segment displays (as two hexadecimal characters)
  Check for correct values of start-bit and stop-bit

## Slide 4: Example: Alarm Level Display with IF-THEN-ELSE
red
orange
yellow
green
Alarm w. Priority 1 (prio1)
Alarm w. Priority 2 (prio2)
Alarm w. Priority 3 (prio3)
Alarmstufe
Notes: In a system are several sources for an alarm.
Some alarms are more sever then others and get Priority 1
The indicator is supposed to ease th recognition of the situation several alarms come at the same time
E.g. if alarm prio 1 is active, the yellow lamp reports a minor problem, but if in additional an alram of priorit 1 is activated, the red lamp indicates a major problem

## Slide 5: Describe a Truth Table with Don’t Care using IF-THEN-ELSE statements
Eingänge |  |  | Ausgänge |  |  | 
Prio1 | Prio2 | Prio3 | grün | gelb | orange | rot
1 | x | x | 0 | 0 | 0 | 1
0 | 1 | x | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0
Notes: The priority example represents an incomplete truth table

## Slide 6
IF bool_expr_1 THEN
sig <= val_expr_1;
ELSIF bool_expr_2 THEN
sig <= val_expr_2;
ELSIF bool_expr_3 THEN
sig <= val_expr_3;
ELSE
sig <= val_expr_4;
END IF;
Priorisation with IF-THEN-ELSE
IF-THEN-ELSE describes
logic with priority

## Slide 7: Synthesis output (RTL Viewer) with Quartus
prio1
prio2
prio3
Notes: When synthesized, the IF-THEN-ELSE again is in the first synthesis step transformed to multiplexers.
The lines with higher priority appear closest to the output
As further down in the IF-THN-ELSE lines we go the inputs move away from the outputs. The prio3 signal has to pass through 2 levels ov multiplexers

## Slide 8: Case Statement in Process
CASE <control input> IS WHEN <test> => {<sequential statements>}; [WHEN <test> => {<sequential statements>};] … [WHEN OTHERS => {<sequential statements>};]
END CASE;

## Slide 9: Beispiel: 4 x 1 Multiplexer mit CASE
ARCHITECTURE comb OF mux_beispiel IS BEGIN muxer: PROCESS(sel,a,b,c,d) BEGIN CASE sel IS WHEN "00" => x <= a; WHEN "01" => x <= b; WHEN "10" => x <= c; WHEN OTHERS => x <= d; END CASE; END PROCESS muxer; END comb;
x
c
b
a
sel
2
2
2
"01"
"10"
"00"
"11"
d
CASE ist NICHT Priorisierend
Notes: A CASE is one method in VHDL to describe combinatorial logic
Case is very similar to a truth table sel is the vector description of the Input of the truth table
Each entry of a line that begins with «WHEN» describes the output behavoiour of that trutj table
If a truth table can not be listed complete (in most cases it is impossible, since a signal is not just 1 or 0 but als o Z, x …) WHEN OTHERS covers all thos unlisted combinations. The compiler checks if all combinations are listed

## Slide 10: Multiplexer nach Synthese mit Quartus
(RTL Ansicht)
Erster Schritt:
Umwandlung in Multiplexer
Notes: The transformation from text input to LCELLs happens in several steps
First step: The synthesizer transforms the CASE statement in Multiplexers

## Slide 11: Examples: Counters

## Slide 12
12
Q
= number of FFs
n
clock
n
n
+
+1
0xf | 1111
+0x1 | 0001
 | 10000
Carry bit (ignored / hardware limitation!)
Overflow when counting up:
0x0 | 0000
-0x1 | 1111
 | 1111
Underflow when counting down:
1) Modulo Counter

## Slide 13: 2) What is the behaviour of this counter?
13
Q
!Q
= number of FFs
n
Takt
n
n
+
+1
1
0
enable
clk
enable
cnt
D
cnt
cnt
cnt + 1
cnt + 2
D

## Slide 14: 3) Counter with Load
14
Q
!Q
= number of FFs
n
Takt
n
n
+
+1
0
1
load_value
load
n
clk
load
cnt
D
cnt n
load_value
l_value + 1
D
cnt n+1
cnt n+2
l_value + 2
l_value + 3
l_value

## Slide 15: 4) Count-down with automatic Reload
15
Q
!Q
= Anzahl der FFs
n
Takt
n
n
+
-1
0
1
„9"
zero
n
clk
zero
cnt
0
2
1
9
8
Dekoder für 0

## Slide 16: 5) Counter with Load and Enable
16
Q
!Q
n
Takt
n
n
+
+1
0
1
load_value
load
n
n
1
0
enable
Welcher Eingang hat Priorität, load oder enable?

## Slide 17: Three Basic RTL Blocks: - counters - shiftregisters - finite state machines (FSM)

## Slide 18: RTL Basic Structure for Counters, Schiftregisters and State-Machines
in_sig
clock
reset_n
S
D Q
R
D Q
out_sig
n
n
reg
next_reg
The RTL basic structure of these three blocks is always the same!
Adapt the signal naming to make clear, which block is implemented
Obs.: here we consider a Moore FSM. Which difference do you expect for a Mealy machine?

## Slide 19: Counter
clock
reset_n
S
D Q
R
D Q
out_sig
n
n
count
next_count

## Slide 20
shift_lsb
serial_in
clock
reset_n
S
D Q
R
D Q
out_sig
n
n
shiftreg
next_shiftreg
LIBRARY ieee;
USE ieee.std_logic_1164.all; USE ieee.numeric_std.all;
ENTITY schieberegister IS PORT( clk,reset_n : IN std_logic;
shift_lsb : IN std_logic;
serial_in : IN std_logic; out_sig : OUT std_logic_vector(3 downto 0) ); END schieberegister;
Shiftregister : example (1/2)

## Slide 21
ARCHITECTURE rtl of schieberegister is
signal shiftreg : std_logic_vector(3 downto 0); signal next_shiftreg : std_logic_vector(3 downto 0);
BEGIN logik : PROCESS (shiftreg, shift_lsb, serial_in) BEGIN IF shift_lsb = '1' THEN next_shiftreg <= serial_in & shiftreg(3 downto 1); ELSE next_shiftreg <= shiftreg(2 downto 0) & serial_in; END IF; END PROCESS logik;
flip_flops : PROCESS (clk, reset_n)
BEGIN IF reset_n = '0' THEN shiftreg <= (OTHERS => '0');
ELSIF rising_edge(clk) THEN shiftreg <= next_shiftreg; END IF; END PROCESS flip_flops;
… -- Output Zuweisung …
END architecture rtl;
Shiftregister : example (2/2)

## Slide 22: Applications of Shiftregisters
PC serial interface or USB interface
Serial data input / parallel data output (parallel-serial conversion)
Parallel data input / serial data output, (serial-parallel conversion
Serial data input / serial data output)
Fast counter with few components
Generation of clock frequencies with different phase
Dividing / multiplying
Generation of pseudorandom sequences

## Slide 23: Basic Structure of Shiftregister
Q
D
!Q
Q
D
!Q
D1
Q0
Q
D
!Q
D2
Q1
IN
FF0
FF1
FF2
CLK
Q
D
!Q
Q2
FF3
D3
Q3
MSB
LSB
Example with shift direction from LSB towards MSB
Notes: What happens with this circuit, when all FF are Q=0 after reset , signal In=1 an a rising edge is applied to CLK? Will all FF Q0 - Q3 switch at the same CLK edge to 1 or only Q0 = 1 and the reset stays 0. If the second case applies, why?
The second case applies, because there is a delay from CLK until Q changes. Q0 remains 0 for a while, during the rising edge of CLK is applies at the CLK input of FF2 and such FF2 stays low.
Only one CLK edge later, also Q1 becomes high. The same repeats for Q2 and Q3.
The one is «shifted» from FF to FF, that is why we call this a shift register
It is importand to note that how the Shift register is shown here, the MSB is contrary to the usual drawings, on the right and LSB on the left. This is because the D input of FF are mostly on the left side of the FF and we read from left to right.

## Slide 24: IEC Symbol for Shiftregister
CLK
Q0
Q1
Q2
Q3
IN
SRG4
C1/
Q
D
!Q
Q
D
!Q
D1
Q0
Q
D
!Q
D2
Q1
IN
FF1
FF2
FF3
CLK
Q
D
!Q
Q2
FF4
D3
Q3

## Slide 25: Parallel to Seriell Conversion (and vice versa)
Parallel | Serial
Q0
Q1
Q2
Q3
LSB
MSB
1 | 1 | 0 | 0
Clock
Data
MSB
LSB
Example:
Printer
Example:
RS232 (UART)
USB
Microprocessorbus (32/64 bit)
Memory IC’s
Notes: On a Parallel Data transfer, the Nibble or Byte that needs to be transferred consists of paralle birs eg. Q0-Q3
On a Serial Data transfer, the Data are transfered sequentially on after another, often accompanied by a clock

## Slide 26: Parallel to Serial Converter
Q
D
!Q
D2
Q3
D1
Q2
OUT
FF3
FF2
FF1
CLK
Q1
FF0
D0
Q0
1
0
Q
D
!Q
1
0
Q
D
!Q
1
0
Q
D
!Q
1
0
D3
Load
MSB
LSB
Example for shift towards LSB
Notes: The input of D-FF are connected to Multiplexers. With the Multiplexer one can choose whether the D Input of a FF is connected to the Q output of the previous FF or (shift Register Mode), or a direct paralle inpuz D0-D3

## Slide 27: Universal Shiftregister 74F194 (only representing 3 bits)
D1
D2
FF1
FF2
CP
Q
D
!Q
00
Q0
Q
D
!Q
11
01
10
00
11
01
10
DSR
FF2
Q
D
!Q
00
11
01
10
DSL
D0
Q1
Q2
S0
S1
S1 | S0 | Function
0 | 0 | Freeze
0 | 1 | Shift to MSB
1 | 0 | Shift to LSB
1 | 1 | Load

## Slide 28: Linear Shiftregister
CLK
Q0
Q1
Q2
Q3
D0
SRG4
C1/
=1
Notes: The following example is a so called «linear shift register» built from a 4-bit shift register. In the 4-bit example, the last MSB of the shift register are xored and fed back to the shift register input.
Linear shift registers are possible with more than 4-bits, but the feed back logic is different.

## Slide 29: State Diagram of linear Shiftregister
8
12
14
10
5
3
9
6
1
7
0
15
4
2
11
13
Maximale Length of Sequence = 2n - 1
Notes: The sequenz of a linear shift register is random considerung the values the 4-bits represent
If the Q outputs of the linear shift register would be connected to a D/A convertre, the output would be white noise
Of course the randomnes repeats after 2n-1 states

## Slide 30: Generic Equations for linear Shiftregisters
Notes: Is a table how linear Shift Registers can be built from 3 to 20 bits.

## Slide 31: Application Example of linear Shiftregister: Pseudo Random Generator (PRG) to cipher a bitstream
Encryption Decryption
Quelle: THE RC4 STREAM ENCRYPTIION ALGORITHM _ William Stallings
Notes: The following example is a so called «linear shift register» built from a 4-bit shift register. In the 4-bit example, the last MSB of the shift register are xored and fed back to the shift register input.
Linear shift registers are possible with more than 4-bits, but the feed back logic is different.

## Slide 32
mode_a
clock
reset_n
S
D Q
R
D Q
out_sig
n
n
state
next_state
LIBRARY ieee;
USE ieee.std_logic_1164.all;
ENTITY automat IS PORT( clk,reset_n : IN std_logic;
mode_a : IN std_logic;
out_sig : OUT std_logic_vector(3 downto 0) ); END automat;
State-Machine : example (1/2)

## Slide 33
ARCHITECTURE rtl of automat is -- Typ declaration (enumerated type) fuer
type fsm_states is (idle, load_a, load_b, enable, wait_cnt);
signal state : fsm_states; signal next_state : fsm_states;
Obs:
With the type declaration the state encoding is not explicitly defined
The Synthesizer-Tool (Quartus) can select and optimise the state encoding to reduce the combinational logic.
In case you need to define the state encoding, do it by defining constants (but in most cases not)
State-Machine : example (2/2)

## Slide 34: Applications of State Machines (automaton)
Control functions in digital systems
Input-related sequential control
Control of a bus interface
Direct memory access in the microprocessor
Command pipeline in the microprocessor
Automaton = Finite State Machine (FSM)
Notes: Finite state machines are «intelligent» controllers
They are very similar to counters. The simplest form is a counter which direction can be controlled by an external signal
FSMs are active Circuits and the engines which drive Bus Interfaces
A DMA is a circuit which actively reads data from one address range in a system and transfers it to another address range in the system, a FSM is the engine of a DMA

## Slide 35: The Moore FSM RTL Diagramm
Q
!Q
Drive Logic
n = number der FFs
n
clock
n
Output- Logic
Et
Et = Input vector
Zt = State vector at current time
Zt+1 = State vector after next clock edge
d
m
Zt
Zt+1 = d (Zt, Et)
At = m (Zt)
m
Notes: The logic in front of the memory is called «Ansteuerlogic» becuase it calculates the next state out of the current state
In moost cases there is not only one controll signal, but several, the control signals are called «Eingangsvector» E. Signal bundles are often called Vectors
Z is the actual state or «Zustandsvector» at actual Time

## Slide 36
State 1 /
000
State 2 /
001
transition
condition 1
transition
condition 2
The Moore FSM
Bubble Diagram (State Diagram)

## Slide 37: Example: Sequence/Pattern Recognition
Recognise the following sequence of the input signal e_in (2 bits wide): „01/11/10“
Once the sequence is recognised the FSM generates an output pulse q_out with the width of one clock period
01
11
10
11
01
00
00
clk
e1_in e0_in
q_out
Draw the RTL diagram of the FSM?
Draw the bubble diagram of the FSM?
11

## Slide 38: Example: Sequence/Pattern Recognition
state
clk
e1_in
e0_in
Drive- logic
Q
D
!Q
2
next state
reset
Moore FSM
q_out
Drive Logic
clocked Process
Output Logic

## Slide 39: Example: Sequence/Pattern Recognition
Z0
00
Z1
01
Z2
11
Z3
10
01
00/10
11
01
11/00
10
00/11/10
00/11/10
01
01
Bubble Diagram
Inputs e1_in e0_in

## Slide 40
Example: Sequence/Pattern Recognition
VHDL Code - Entity

## Slide 41
Example: Sequence/Pattern Recognition
VHDL Code architecture : drive logic

## Slide 42
Example: Sequence/Pattern Recognition
VHDL Code architecture: flip-flops and output comb-logic

## Slide 43
BeExample: Sequence/Pattern Recognition
Simulated Timing Diagram
q_out
state
next_state
Source: Lehrbuch Digitaltechnik : eine Einführung mit VHDL / Reichardt

## Slide 44: Example: Sequence/Pattern Recognition
Z0
00
Z1
01
Z2
11
Z3
10
01
00/10
11
01
11/00/10
10
00/11/10
00/11/10
01
01
Is there a short-cut (more compact design version)?
Inputs e1_in e0_in
Set output during transition, once e_in = „10“ is detected

## Slide 45
Example: Sequence/Pattern Recognition
VHDL Code of Short-Cut
Variation 1: Moore-FSM
Output depends
only on state (FFs output only)
Variation 2: Mealy-FSM depends additionally on inputs, e.g. e_in

## Slide 46: Example: Sequence/Pattern Recognition
state
clk
e1_in
e0_in
Drive- logik
Q
D
!Q
2
next state
reset
q_out
Drive Logic
clocked Process
Output Logic
2
.
Mealy FSM: outputs also depends directly on input signals

## Slide 47
Example: Sequence/Pattern Recognition
Simulated Timing Diagram with Short-Cut (Mealy)
q_out
aktuell_z
folge_z
Source: Lehrbuch Digitaltechnik : eine Einführung mit VHDL / Reichardt
Dangerous: can produce glitches

## Slide 48: UART Serial Protocol Universal Asynchronous Receiver-Transmitter

## Slide 49: Émile Baudot invented the ASCII Code predecessor
Émile Baudot
1845 - 1903

## Slide 50: UART early Applications
9600 Baud Terminal
300 Baud Akustikkoppler
9600 Baud Industriesteuerung
1200 Baud Modem
9600 Baud CNC Steuerung

## Slide 51: UART-IF Example : Bluetooth Module RN42
UART Port des BT Modules
CTS: Clear to Send
RTS: Ready to Send
TX: Transmit data
RX: Receive data

## Slide 52: UART Hardware Handshake

## Slide 53: UART Hardware Handshake
CTS Function
RTS Function (not used)
Seen from the side of the Bluetooth Module

## Slide 54: Bluetooth Module RN42

## Slide 55: VHDL_02: More RTL Block Design
Laboratory
  Design of a UART receiver (UART-RX) with:
  Baud rate: 31250 bits per second, no parity bit
  Serial input via GPIO pin in extension header of the board
  Display each received byte into two seven segment displays (as two hexadecimal characters)
  Check for correct values of start-bit and stop-bit

## Slide 56: Sampling the Serial Datastream
Stop
start_bit
T
½ T
baud_tick
Bit-Count
stop bit
(logic 1)
data byte
(8 bits)
stop bit
(logic 1)
T
Start
1 2 3 4 5 6 7 8 9 10

## Slide 57: Block Diagram of UAR(T) DIVIDE AND CONQUER
sync_n_ edge_det
RX_FSM
tick_
generator
RX_ registers
sev_seg decoders
from GPIO
to HEX[6..0]